## Slide 1: GOA Calculator
By: Asad Mirza
CV-PEUTICS

## Slide 2: What is GOA?
= Area enclosed by planar boundaries

## Slide 3: ANSYS Structural Simulation
Material properties – Mooney Rivilin (2nd order)
Boundary Condition:
  Radial Displacement: 6 mm
  Frictionless Support on top/bottom of inlet/outlet.
High element quality mesh and convergence of 1x10-6 set for all equations.

## Slide 4: Grayscale
Signal to noise: Color information not important for finding edges of GOA area.
Complexity of code / Speed: Color is a MxNx3 matrix while grayscale is just MxN.

## Slide 5: Image Contrasting
Map intensity of values from default range to constrained range.

## Slide 6: Gaussian Blur
Blur center and surrounding pixels, emphasizes edges.

## Slide 7: Graph Cut
Pixels are nodes
Valve/Not Valve = Source/Sink
Add cost to each node
Find most efficient cut

## Slide 8: Flood Fill
Select starting point in background.
Algorithm fills in region up to boundaries of foreground.

## Slide 9: Active Contour
Fills in regions smaller than specified size.
Results in only largest region remaining.

## Slide 10: Area Extraction
Summation of total number of pixels (n) in image (I) that are white.
Convert from pixel area to cm2 using calibration scale.
GOA = 0.8 cm2

## Slide 11: Summary Workflow
A
B
C
D
E
F
G

## Slide 12: Results

## Slide 13: Next Steps
Validate GOA with echo/CT derived values in literature.
Streamline code for optimization of image processing
  Current ETA for 1 image: 2.5 seconds.
  Current ETA for 1 video (~200 frames): 8.3 minutes